## Slide 1: Thermally Actuated Flexure
PRECISION MACHINE DESIGN
Members: Michael Erickson
Chunjie Fan
Gokul Mohandas
Ameya Parab

## Slide 2: Objectives
Evaluate load capacity of flexure to displace 1000N loads 100um
Achieve position control within 100 µm range under various loads
Thermally isolate the actuator.
Decrease the response time of the flexure.

## Slide 3: Original Design
Compound flexure, single degree of freedom
Heated aluminum tube actuator
Thermal isolation of actuator
PWM heater and water pump control
Aluminum frame susceptible to deflection during actuator expansion
Aluminum tube actuator
Water cooling lines
Ni-Cr Coil
Glass
Knife holder
Knife
Knife edge displacement sensor
Flexure table
Aluminum frame

## Slide 4: New design
Monolithic rigid steel frame
Load application compression system
Position guide pins for flexure table
Thermal isolation of actuator
PID heater and water pump control
Cooling lines
Ni-Cr Coil
Compression system
Guide pins
Displacement sensor
Temperature sensor
Displacement sensor
Knife
(flexure motion)

## Slide 5: Manufacturing
1018 Steel frame
Compression system
Spring guide
Adjustable guide pins
Set screws
Guide pins
Knife holder
Ni-Cr coil

## Slide 6: Deformation of original design
Base structure deflection with 1000N load
Maximum axial deflection = 431.1 µm

## Slide 7: Frame deformation (Aluminum Vs Steel)
Maximum axial deflection
6061 Aluminum 1.8 µm
1018 Steel 0.6 µm
Frame deflection with 1000N axially along actuator
Total axial deflection
1018 Steel 8 µm
Frame only
Frame and base
Fixed
Force
Fixed base
Force
Fixed
1018 Steel was chosen from frame material

## Slide 8: Optical sensor calibration
Displacement to voltage relationship
Micrometer displacement
5 um increments
300 um range
Optical sensor
Micrometer

## Slide 9: Optical sensor calibration
Chart: Voltage(V)
Linear range over ~200 um
52:1 ratio

## Slide 10: Control system flow chart

## Slide 11: Test: 100um displacement
Applied force
Flexure motion
Compression screw
Procedure:
Applied 0N – 1000N to flexure and displaced flexure stage by 100um under each load
Spring constant – 294 lb/in
Turns per inch – 24
1.8 screw rotations for 100N increase
Measurands:
Actuator’s force capability
Parameters:
Room temperature 23C
Results were peformed using cooling water flowing through actuator tube.
Boolean control of actuator 12V power supply
Actuator coil resistance ~1.5Ω

## Slide 12: Results: 100um displacement Cooling water was flown threw actuator upon cooling
Applied force
Flexure motion
Compression screw
Chart: Heating to 100um
Cooling time constants
~0um – 100um
t0N = 15s
t500N = 25s
Heating time constants* ~0um – 100um
t0N = 60s
t500N = 55s
Heating 12V only
Cooling only
*Time constants are determined by heating initialization to 100um displacement.

## Slide 13: Results: 100um displacement
Applied force
Flexure motion
Compression screw
Heating time constants* 0um-100um
t500N = 60s
t1000N = 65s
Chart: Heating to 200um
Heating 12V only
*Time constants are determined by heating initialization to 100um displacement.

## Slide 14: Test: Thermal isolation of actuator
Procedure:
Under 200N displaced at 100um, evaluated temperature of flexure stage and frame
Measurands:
Temperature of the flexure stage
Temperature of frame surrounding actuator
Parameters
Applied load 200N
Flexure stage displaced ~0um – 100um
Room temperature 23C
Cooling water
Table temp
Heat source
Frame temp

## Slide 15: Test: Thermal isolation of actuator
Cooling water
Table temp
Heat source
Frame temp
Chart: Temperature(°C) - Flexure stage
0um
100um
Room temperature
23°C
Increase in frame temp
0.4212°C
Increase in table temp
0.5188°C

## Slide 16: Test: Positional control and stability
Procedure:
Under 100N, 500N, and 1000N flexure stage was displaced to commanded positions are held steady for a time
Measurands:
Flexure stage position
Error
Parameters
Cooling achieved using 4”x4” box fan targeted at coil (no cooling water was used through actuator)
Room temperature 23C
Force
Displacement
Heat

## Slide 17: Results: 0N Positional control and stability
Chart: Displacement by controlling Ni-Cr coil under 0N pre-load
Chart: Error (desired - measured position) (µm) 0N pre-load
Chart: Variation of Table and Frame temperatures 0N pre-load

## Slide 18: Results: 500N Positional control and stability
Chart: Displacement by controlling Ni-Cr coil under 500N pre-load
Chart: Error (desired - meaured position) (µm) 500N pre-load
Chart: Variation of Table and Frame temperatures 500N pre-load

## Slide 19: Results: 1000N Positional control and stability
Chart: Displacement by controlling Ni-Cr coil under 1000N pre-load
Chart: Error (desired - meaured position) (µm) 1000N pre-load
Chart: Variation of Table and Frame temperatures 1000N pre-load

## Slide 20: Results: 1000N zoom at 50um
Chart: 1000N pre-load
Chart: Displacement by controlling Ni-Cr coil under 1000N pre-load
Chart: Error (desired - meaured position) (µm) 1000N pre-load
Average error
error = (-)0.33 um

## Slide 21: Heating time constants for 0um to 30um displacement
Chart: 0N pre-load
Chart: 500N pre-load
Reason why t1000N < t500N may be friction on flexure stage from guides pins
Time constants
~0um – 30um
t0N = 235.2s
t500N = 578.6s
t1000N = 535.1s
Chart: 1000N Pre-load
Desired = 25um
Time constants for error = 10%

## Slide 22: Bill of materials, mechanical
 | Item | Description | Material | Total Cost
Frame | Steel Plate | 0.75’’ thick, 8’’x24’’, 2 ft. length | 1018 steel plate | 133.01
 | Screw | Fastening actuator side for frame, 10-24 thread,5"1/2" lg. | Black-Oxide Alloy Steel | 6.38
 | Screw | Fastening spring side of frame, 10-24 thread, 4 3/4" length | Black-Oxide Alloy Steel | 5.92
 | Washer | Flat type washer with ID 0.203", OD 0.438", Thickness 0.024"-0.038" | 316 Stainless Steel | 4.24
 | Hex Standoff | 5/8'' OD, 1/4''-20 , 3 1/2" length, Female thread | 2011 Aluminum | 3.36
 | Nut | 10-24, 1/8" thick, pack of 100 | 18-8 Stainless Steel | 3.50
Actuator | Steel drive tube | NPT Male Threaded on Both Ends, 1/8 Pipe Size, 4" Long | 304/304L Stainless Steel | 3.18
 | Aluminum drive tube | NPT Male Threaded on Both Ends, 1/8 Pipe Size, 4" Long | Aluminum | 2.08
 | Brass hose barb | 1/8 FNPT, 1/4" tube size, barbed, 90deg elbow | Brass | 17.36
 | Guide rods (flexure stage) | 0.1990" OD 3 ft. 6 ft. | Tool Steel | 6.50
 | Set screws | Oval tip, 1/4''-20 thread size, 1'' length, Hex Coarse thread set screws | Alloy Steel | 10.17
 | Guide pins (compression screw) | 1/4" OD, 3'' length, dowel pin | Hardened Alloy Steel | 8.03
 | Knurled-Rim Knob | 5/16"-24 x 1-3/4" Threaded Stud, 1-1/2" Diameter | Black-Oxide Steel | 5.59
 | Compression Spring | Zinc-Plated, Music-Wire, Closed & Flat Ends, 2" Long, 3/4" OD, 294 lb/in | Zinc-Plated Music-Wire Steel | 17.61

## Slide 23: Bill of materials, mechanical and electrical
Actuator | Steal bar stock | 1/4" thick, 3/4" wide, 2 ft. length rectangular bar | Low-Carbon Steel | 20.34
 | Aluminum shaft stock | 15" OD (for spring guide) | 6061 Al | 
 | Ni-Cr wire | 0.064" Diameter, 1/4 lb. Spool, 21' Long | Nickel Chromium | 21.28
Cooling and isolation | Round Seal | O-Ring Cord Stock, 1/4" OD, 3' length. | Neoprene Rubber | 1.65
 | Plastic tubing | Durometer 50A, 1/8" ID, 1/4" OD, 375F, 10ft | Silicone Rubber | 6.9
 | Plastic tubing | Cooling Pipes | PVC | -
 | Glass | For low friction surface for guide rods against flexure | Glass | -
Controls | myRIO | Controller | - | -
 | 16 bit ADC | Analog to Digital Converter | - | -
 | 12V 10A power supply | TDK Lambda | - | -
 | Power amplifier | Amplifier | - | -
 | ± 12 V Power supply | RIGOL Power Supply | - | -
 | Temperature sensors | LM 35 | - | -
 | Optical Sensor | RPI 0352E | - | -
 | TOTAL |  |  | $ 277.10
 | Item | Description | Material | Total Cost

## Slide 24: Project milestones
Objective | Start date
Evaluate current design, finalize dimensions and material specifications | Sunday March 9th
Order materials | March 20th
Frame Manufacturing | April 6th
Assemble new design | April 17rd
Testing, calibration, modifications | April 24th
Final Results | May 1st, 2017
Final Presentation | May 4th, 2017

## Slide 25: Future improvements
Increase compression force
Fine tune controller
Create improved method to mount actuator
More sensitive pumps; more controllable flow
Improve electrical isolation between Ni-Cr wire and actuator tube